## Slide 1: Introduction
K-map is the best manual technique for the simplification of Boolean equations, but it becomes difficult to manage when number of variable exceed 5 or 6.
So a technique called map entered variable (MEV) is used to increase the effective size of k-map.
It allows a smaller map to handle a large number of variables.

## Slide 2: Introduction
Let m denote the number of squares in a k-map and let n be the number of variables then
m=
If we use the MEV then number of squares (m) will be reduced.
MEV k-map allows us to enter a single variable (A,B,…etc) or a complete switching expression(such as A+B’C) into a cell, in addition to 0s,1s and don’t care terms.

## Slide 3: Example
Question:
Simplify y=f(A,B,C,D)=∑m(1,4,5,6,9,12) and y should be zero for inputs 0,2,3,7,10,11 and the remaining possible codes never occur in system using MEV k-map technique. Consider D as MEV.

## Slide 4
Minterm | A | B | C | D | Y | Y(Reduced)
0 | 0 | 0 | 0 | 0 | 0 | D
1 | 0 | 0 | 0 | 1 | 1 | 
2 | 0 | 0 | 1 | 0 | 0 | 0
3 | 0 | 0 | 1 | 1 | 0 | 
4 | 0 | 1 | 0 | 0 | 1 | 1
5 | 0 | 1 | 0 | 1 | 1 | 
6 | 0 | 1 | 1 | 0 | 1 | 
7 | 0 | 1 | 1 | 1 | 0 | 
8 | 1 | 0 | 0 | 0 | 0 | D
9 | 1 | 0 | 0 | 1 | 1 | 
10 | 1 | 0 | 1 | 0 | 0 | 0
11 | 1 | 0 | 1 | 1 | 0 | 
12 | 1 | 1 | 0 | 0 | 1 | 
13 | 1 | 1 | 0 | 1 | 0 | 
14 | 1 | 1 | 1 | 0 | 0 | 0
15 | 1 | 1 | 1 | 1 | 0 | 
Minterm | A | B | C | D | Y | Y(Reduced)
0 | 0 | 0 | 0 | 0 | 0 | D
1 | 0 | 0 | 0 | 1 | 1 | 
2 | 0 | 0 | 1 | 0 | 0 | 0
3 | 0 | 0 | 1 | 1 | 0 | 
4 | 0 | 1 | 0 | 0 | 1 | 1
5 | 0 | 1 | 0 | 1 | 1 | 
6 | 0 | 1 | 1 | 0 | 1 | 
7 | 0 | 1 | 1 | 1 | 0 | 
8 | 1 | 0 | 0 | 0 | 0 | D
9 | 1 | 0 | 0 | 1 | 1 | 
10 | 1 | 0 | 1 | 0 | 0 | 0
11 | 1 | 0 | 1 | 1 | 0 | 
12 | 1 | 1 | 0 | 0 | 1 | 
13 | 1 | 1 | 0 | 1 | 0 | 
14 | 1 | 1 | 1 | 0 | 0 | 0
15 | 1 | 1 | 1 | 1 | 0 | 
Truth Table

## Slide 5: Reduced expression using k-map
A\BC | 00 | 01 | 11 | 10
0 | D |  |  | 1
1 | D |  |  | 
A\BC | 00 | 01 | 11 | 10
0 | D |  |  | 1
1 | D |  |  | 
Y = + + B
= (B⊕C) +

## Slide 6: VEM with two MEV
Suppose y=A’B’C’D’+A’B’CD’+ABCD+AB’CD+AB’CD’
then plot VEM by considering C and D as MEV.

## Slide 7
Minterm | A | B | C | D | Y | Y(Reduced)
0 | 0 | 0 | 0 | 0 | 1 | + C
1 | 0 | 0 | 0 | 1 | 0 | 
2 | 0 | 0 | 1 | 0 | 1 | 
3 | 0 | 0 | 1 | 1 | 0 | 
4 | 0 | 1 | 0 | 0 | 0 | 0
5 | 0 | 1 | 0 | 1 | 0 | 
6 | 0 | 1 | 1 | 0 | 0 | 
7 | 0 | 1 | 1 | 1 | 0 | 
8 | 1 | 0 | 0 | 0 | 0 | C + CD
9 | 1 | 0 | 0 | 1 | 0 | 
10 | 1 | 0 | 1 | 0 | 1 | 
11 | 1 | 0 | 1 | 1 | 1 | 
12 | 1 | 1 | 0 | 0 | 0 | CD
13 | 1 | 1 | 0 | 1 | 0 | 
14 | 1 | 1 | 1 | 0 | 0 | 
15 | 1 | 1 | 1 | 1 | 1 | 
Minterm | A | B | C | D | Y | Y(Reduced)
0 | 0 | 0 | 0 | 0 | 1 | 
1 | 0 | 0 | 0 | 1 | 0 | 
2 | 0 | 0 | 1 | 0 | 1 | 
3 | 0 | 0 | 1 | 1 | 0 | 
4 | 0 | 1 | 0 | 0 | 0 | 0
5 | 0 | 1 | 0 | 1 | 0 | 
6 | 0 | 1 | 1 | 0 | 0 | 
7 | 0 | 1 | 1 | 1 | 0 | 
8 | 1 | 0 | 0 | 0 | 0 | 
9 | 1 | 0 | 0 | 1 | 0 | 
10 | 1 | 0 | 1 | 0 | 1 | 
11 | 1 | 0 | 1 | 1 | 1 | 
12 | 1 | 1 | 0 | 0 | 0 | CD
13 | 1 | 1 | 0 | 1 | 0 | 
14 | 1 | 1 | 1 | 0 | 0 | 
15 | 1 | 1 | 1 | 1 | 1 | 
Truth Table

## Slide 8: Reduced expression using k-map
A\B | 0 | 1
0 | + C | 
1 | C + CD | CD
A\B | 0 | 1
0 |  | 
1 |  | CD
Y = ACD + C +
= ACD + (C + )
= ACD + (C + )

## Slide 9: Advantages of VEM
The variable entered map can be used to plot an n-variable problem on n-1 variable map.
The variable entered map occurs in design problems involving multiplexers , which can be solved more readily by this approach than by k-maps.

## Slide 10: Quine McCluskey Method
Some Facts About Quine McCluskey
Developed in 1956
Also known as Tabulation Method
Used for Minimization of Boolean Functions
Where Karnaugh Map could solve for upto 5 bits, Quine McClusky can solve for more than 5 bits.
Has easy algorithm than Karnaugh, so it is efficient and can be easily implemented in computer algorithms.

## Slide 11
Steps
Four main Steps:
1. Generate Prime Implicants
2. Construct Prime Implicants Table
3. Reduce Prime Implicants
4. Solve Prime Implicants table

## Slide 12
Example Problem
 Σ (0,4,5,7,10,12,13,14,15)
Step-1: Listing the Binary codes of each number.
No Binary
0 | 0000
4 | 0100
5 | 0101
7 | 0111
10 | 1010
12 | 1100
13 | 1101
14 | 1110
15 | 1111
Table 1

## Slide 13
Step-2: Listing Binary Numbers according to their number of 1’s as in Table.2
Step-3: Making Table of Duals from Table:2
Step:2 Table 2
Step:3 Table 3
Table:2
 | ABCD | 
0 | 0000 | X
4 | 0100 | X
5 | 0101 | X
10 | 1010 | X
12 | 1100 | X
7 | 0111 | X
13 | 1101 | X
14 | 1110 | X
15 | 1111 | X
0,4 | 0_00
4,5 | 010_
4,12 | _100
5,7 | 01_0
5,13 | _101
10,14 | 1_10
12,13 | 110_
12,14 | 11_0
7,15 | _111
13,15 | 11_1
14,15 | 111_

## Slide 14
Step-4: Generating table of Quads from Table.3
ABCD
ABCD
Table:4
Table:3
 | ABCD | 
0,4 | 0_00 | PI
4,5 | 010_ | X
4,12 | _100 | X
5,7 | 01_0 | X
5,13 | _101 | X
10,14 | 1_10 | PI
12,13 | 110_ | X
12,14 | 11_0 | X
7,15 | _111 | X
13,15 | 11_1 | X
14,15 | 111_ | X
 | ABCD | 
4,5 12,13 | _10_ | PI
4,12 5,13 | _10_ | 
5,13 7,15 | _1_1 | PI
5,7 13,15 | _1_1 | 
12,13 14,15 | 11__ | PI
12,14 13,15 | 11__ | 

## Slide 15
Step-5: Making table of Prime Implicants
?
Prime
0
4
5
7
10
12
13
14
15
Implicants
0.4


10.14


4.5-12.13
5.13-7.15
12.13-14.15












0.4 + 10.14 + 5.13-7.15 + 4.5-12.13

## Slide 16
Step-6: Generating SOP from Prime Implicants
0,4 + 10,14 + 5,13,7,15 + 4,5,12,13
Now Since
PI
So the minimized SOP is: A’C’D’ + ACD’ + BD + BC’
PI | ABCD
0,4 | 0_00
10,14 | 1_10
5,14 7,15 | _1_1
4,5 12,13 | _10_

## Slide 17
THANK YOU